## Slide 1
Rafsan Jany
Korean Convergence Medical Science
A Cross-Modal ECG–SQUID MCG Representation Learning Framework

## Slide 2
1
What is SQUID Magnetocardiography (MCG)
MCG = Magnetic ECG measured using SQUID devices
SQUID = Superconducting Quantum Interference Device
Most sensitive magnetic sensor in the world
Detects magnetic fields produced by the heart
Unlike ECG, magnetic fields aren’t distorted by body tissues
Can reveal cardiac abnormalities that ECG may miss
Used today mainly in research centers (rare & expensive)
Fenici et al., European Heart Journal, 2020
Park et al., Sensors, 2020
Koch et al., Biomedical Engineering Online, 2011

## Slide 3
2
Why MCG matters (Clinical motivation)
MCG can detect:
Ischemia earlier than ECG
Conduction abnormalities
Fetal arrhythmias (when ECG is unreliable)
Subtle repolarization changes
Spatial current distribution of the heart
Problem:
Almost no hospitals use MCG — devices are rare, expensive, and datasets are tiny.
This makes AI or deep-learning on MCG nearly impossible.

## Slide 4
3
The Current Gap
Gap 1 — MCG Technology Is Underutilized in Clinical Practice
SQUID-MCG can detect ischemia, fetal arrhythmia, and subtle conduction delays
But MCG is rare, expensive(cost $1M+), and only available in research centers
Gap 2 — ECG Alone Cannot Capture Everything
ECG signals get distorted by tissue, muscle, fat
MCG is cleaner, but too rare
Clinicians lack a unified view combining both modalities
Gap 3 — There Are Almost No MCG Datasets for AI
Only one open-access dataset contains real SQUID-MCG: Koch et al. (2011)
It is extremely small (127 beats)
Makes modern AI training impossible without new methods
Gap 4 — No way to help hospitals without SQUID machines
If we could use ECG to approximate MCG
Many hospitals could benefit from MCG insights
But no such system exists today
Probable Solution
We need a way to learn MCG representations without needing thousands of MCG recordings.

## Slide 5
4
Core Research Idea
ECG and MCG measure the same heart activity, but each sees a DIFFERENT part of
the truth.
ECG beat → vector (electrical potential ON the skin)
MCG beat → vector (magnetic field generated by the SAME currents INSIDE the heart)
Both vectors are close if they come from the same heartbeat.
Simple Word:
ECG and MCG are like two cameras taking a picture of the same object from different angles.
→ Both capture the heartbeat.
→ Both look at the same depolarization/repolarization.
→ Both detect conduction abnormalities.
BUT they see different distortions and different hidden details.
ECG → foundational cardiac patterns
MCG → rare, high-value complementary info
Core Research Idea
This study proposed: A model connects electrical and magnetic views of the same heartbeat to provide a more complete cardiac understanding.
The input to the trained model can be either an ECG alone, an MCG alone, or both — because the model
learns a shared representation for both modalities. A shared latent heartbeat representation for
clinical use.

## Slide 6
5
Dataset
PTB Diagnostic ECG Dataset
Source: PhysioNet / PTB Diagnostic ECG Database
Signals: 12-lead ECG
Sampling Rate: 1000 Hz
Subjects: 290+
Conditions: Myocardial infarction, arrhythmia, block, hypertrophy, healthy controls
Size: Thousands of heartbeats (large dataset)
PTB gives us a strong, robust ECG understanding before we try to align ECG with MCG.
Koch ECG–MCG (SQUID) Paired Dataset
Source: Koch et al., Biomedical Engineering Online (2011)
Modalities:
BSPM (Body Surface Potential Mapping) → electrical activity
        32 channels
        1000 Hz
MCG (Magnetocardiography) using SQUID
        100 channels
        1000 Hz
        Femto-Tesla units (fT)
MRI torso scans

## Slide 7
INPUT
6
Methodology Overview
Stage 1 — Learn ECG features from a large dataset (PTB Diagnostic ECG)
Self-supervised learning (no labels needed)
Model learns patterns of electrical activity
Stage 2 — Align ECG with MCG using paired data (Koch dataset)
For each heartbeat: ECG signal ↔ MCG signal
Use contrastive learning to match them in a shared space
Stage 3 — Align ECG with MCG using paired data (Koch dataset)
PTB ECG
Koch ECG
Koch MCG
ECG Encoder
ECG Encoder
MCG Encoder
Projection
Projection
(paired beats)
Shared Latent Space
Alignment
OUT

## Slide 8
7
Conclusion
In this project we propose to:
Self-supervised learning (no labels needed)
Build the first cross-modal representation between ECG and MCG
Overcome MCG data scarcity using contrastive learning
Explore a new direction for cardiac AI research
Enable practical future applications like virtual MCG, enhanced diagnosis, and multimodal fusion
Status:
Dataset (ready)
Preprocessing complete (initially done)
Model design complete ( 0n progress: experimented with 1d CNN )
Training (Next Step)
Evaluation (Next Step)

## Slide 9
8
Thank You